Reducing Spray Drift and Damage

Quick Checklist

Note: Spray drift increases when an increasing number of these conditions are not met.

My nozzle types and operating pressures produce a coarse spray quality

I am using glyphosate, MCPA or 2,4-D products with a very coarse or extra coarse spray quality.

My booms height achieves double overlap at the top of stubble – typically 50cm above the top of weeds for a 110˚ nozzle at 50cm boom spacing.

There are no inversion conditions present - check for inversion warnings or signs of inversions before spraying and stop spraying immediately if a surface temperature inversion or any other unsuitable weather conditions develop.

I am spraying during the day. Do not spray during the period from 1 ½ hours before sunset  until 1 ½ hours after sunrise, unless there is no surface temperature inversion present. (Note: There is a very low risk of temperature inversions when there is full cloud cover and/or wind speed is continuously over 11km/hr).

I am spraying when the wind is blowing away from nearby susceptible plants, crops, houses and towns which are within a kilometre. Do not spray when little, no wind or variable winds.

I am spraying 2,4-D and MCPA products only when the winds are between 3 and 15 to 20 km/hr as measured at the application site (depending on lable conditions).

My application speed is below 18km/hr (industry best practice)

My application speed will be above 18 km/hr but boom height is never more than 50 cm above the target weed or stubble. I am using coarse, very or extra coarse spray quality at the target, no inversion conditions exist during the application period and wind speed is consistently between 3 and 15 to 20 km/hr.

I am monitoring and recording any changes in weather conditions during application including change in wind direction and speed, temperature and presence of inverstion conditions.

I have within 24 hours recorded application details and on-site weather (wind speed, direction, temperature, relative humidity) at the start and end of spraying and at least for every load during spraying.

I am applying a Group I herbicide (2,4-D, 2, 4-DB, MCPA, dicamba, triclopyr, picloram, clopyralid and fluroxypyr):

- I have a Prescribed Chemical Users (PCU) qualification

- I am recording the necessary details as per mandatory state regulations on record keeping for Group I herbicides within 24 hrs

18 June 2014

Biosecurity SA- Rural Chemicals Operations | Phone: 1300 799 684 | Email: PIRSA.RuralChemicals@sa.gov.au